## Slide 1: A mathematical modeling for the stowage planning problem
Kiyoshi, TAKEDA
Yagiura lab

## Slide 2: Outline
Background
Problem Definition
Modeling
Computational experiment
future work

## Slide 3: Background
A carrier ship carries various loads through some ports.
We consider the ship that carries various type of cars. (e.g. passenger car, truck, wrecker, bulldozer...)
Assignment of cars to ship is planned manually.
We aim to make assignment automatically

## Slide 4: Background
Planning assignments that make it easy to load and unload cars is important.
  To avoid human errors
We also have to pay attention to the balance of the total load of the ship
  Unbalanced assignments may result in a sinking.

## Slide 5: Problem Definition
We consider the ships which has 12 decks(floors).
Each deck has up to 4 holds
４
３
２
１

## Slide 6: Problem definition
Given information are as follows.
  Order Information
  Hull(ship) information

## Slide 7: Stowage plan
We assign cars in every order to the hold.

## Slide 8: Mathematical Modeling
We model this assignment based on interviews with planners.
I and Mr.Ukawa made model for this assignment last year.
I will explain constrains and objectives one by one.

## Slide 9: The objectives
the objective function would be the weighted sum of the following five
avoiding multiple orders in one hold
placing same orders by port closer together
choosing a path that is easy for cars to pass
No dead space
placing empty space close to the entrance

## Slide 10: avoiding multiple orders in one hold
we minimize the number of orders with different destinations in different loading areas for each hold.

## Slide 11: placing same orders by port closer together
it is easy to load and unload cars if same orders by port is placed closer

## Slide 12: choosing a path that is easy for cars to pass
There are holds to go through when loading and unloading.
If that hold is full, it will be harder to pass through them.
If so, some cars, we need to move cars in that hold once and bring them back again.

## Slide 13: No dead space
There are some holds with a ramp connecting the deck to the deck.
Once these holds are filled to a certain extent, it will be impossible to reach the deeper holds.

## Slide 14: placing empty space close to the entrance
It often happens that orders are added just before the voyage.
To handle that situation, we should place empty space close to the entrance

## Slide 15: Constraints
Travel routes in the ship
Weight balance of cargo
Rules for splitting orders
Height of the hold

## Slide 16: Travel paths in the ship
There must be a certain amount of space in the path of the car.

## Slide 17: Weight balance of cargo(Forward and backward direction)

## Slide 18: Weight balance of cargo(Left-right direction)

## Slide 19: Rules for splitting orders
For large orders, we have to split them up.

## Slide 20: Height of the hold
Each hold has height.
To place cars in holds, the height of the car needs to be lower than the height of the hold

## Slide 21: Computational experiment
With this model, we confirmed that we can get a good assignment for small booking.
The number of orders and the number of loading and unloading ports increases, the calculations may not be sufficiently advanced in a limited time.[1]
[1]鵜川知哉, 自動車運搬船における貨物積載プラン ニングの席割問題に対する数理モデリング, 修士 論文，名古屋大学情報学研究科, 2020

## Slide 22: Computational experiment
We compared the case with and without considering the height constraint.
The booking we used has 109 orders, has 2 loading ports and 3 destination ports.

## Slide 23
Without height constraint
with height constraint
Calculation time | Objective's value | Lower bound
537 | 1035446 | -4461.98
933 | -4285 | -4461.98
2510 | -4301 | -4461.98
2973 | -4311 | -4461.98
Calculation time | Objective's value | Lower bound
3100 | 385282 | -4461.98
3128 | -4152 | -4461.98
8433 | -4173 | -4461.98
10484 | -4347 | -4461.98

## Slide 24: Computational experiment
We also try to investigate what scale of bookings can be solved in a limited time.
We set the limit time to 24 hours.

## Slide 25
Num of orders | Num of loading ports | Num of Destination ports | when a feasible solution was found. | Value after 1h | Lower bound after 1h | Value after 24h | Lower bound after 24h
109 | 2 | 3 | 537 | -4301.36 | -4461.98 | -4388.44 | -4461.98
109 | 2 | 5 | 1674 | -3522.82 | -4461.98 | -4264.69 | -4461.98
109 | 4 | 3 | 344 | -3515.46 | -4461.98 | -4365.89 | -4461.98
250 | 2 | 3 | 2381 | -3155.02 | -4461.98 | -4083.18 | -4461.98
350 | 2 | 3 | 2249 | -2738.00 | -4461.98 | -2883.58 | -4461.98

## Slide 26: future work
creating an index to evaluate the quality of the assignment
Modifying the mathematical model
Creating heuristic to be able to solve large bookings