## Slide 1: A mathematical modeling for the stowage planning problem
Kiyoshi, TAKEDA
Yagiura lab

## Slide 2: Outline
Background
Problem Definition
Modeling
Computational experiment
future work

## Slide 3: Background
A carrier ship carries various loads through some ports.
We consider the ship that carries various type of cars. (e.g. passenger car, truck, bulldozer...)
Assignment of cars to ship is planned manually.
We aim to make assignment automatically

## Slide 4: Background
There are a lot of things that has to be considered
  Planning assignments that makes it easy to load and unload cars is important.
  Human error should not happen.
  Unbalanced assignments may result in a sinking.

## Slide 5: Problem Definition
We consider the ships which has 12 decks(floors).
Each deck has up to 4 holds
４
３
２
１

## Slide 6: Problem definition
Given information are as follows.
  Order Information
  Hull(ship) information
  order information

## Slide 7: Stowage plan
We assign cars in every order to the hold.
  The order ID 0 is assigned the 3rd hold of 1st deck.
  The order ID 5 is assigned the 2rd hold of 4th deck.

## Slide 8: Mathematical Modeling
We model this assignment based on interviews with planners.
I and Mr.Ukawa made model for this assignment last year.
I will explain objective function and constraints one by one.

## Slide 9: The objective function
the objective function would be the weighted sum of the following five.
avoiding multiple orders in one hold
placing same orders by port closer together
securing a path to prevent loss of work efficiency
No dead space
placing empty space close to the entrance

## Slide 10: avoiding multiple orders in one hold
When an order is unloaded from a hold at a certain port, if there are several orders with different destinations in the same hold, human error may occur.
we minimize the number of orders with different destinations in different loading areas for each hold.
e.g. when unloading at port A
Port A
Port B
Port C
We add a penalty of two to the objective function

## Slide 11: placing same orders by port closer together
it is easy to load and unload cars if same orders by port is placed closer.
We defined a pair of adjacent holds.
we minimize the number of orders with different ports that exist in adjacent pairs of holds.
        ○ ×
Port A
Port B
Port C

## Slide 12: Securing a path to prevent loss of work efficiency
When a hold is full, it would be harder to pass through that hold.
we need to move cars in that hold once and bring them back again.
This leads to a loss of work efficiency.
If this situation occurs in a model, we add a penalty to the objective function

## Slide 13: No dead space
There are some holds with a ramp connecting the deck to the deck.
Once these holds are filled to a certain extent, it will be impossible to reach the deeper holds.
  This space is called “dead space”
We minimize the number of dead space.
90% full
60% full
50% full
60% full
These space are called dead space

## Slide 14: placing empty space close to the entrance
It often happens that orders are added just before the voyage.
To handle that situation, we should place empty space close to the entrance
The entrance

## Slide 15: Constraints
Travel routes in the ship
Weight balance of cargo
Rules for splitting orders
Height of the hold

## Slide 16: Travel paths in the ship
we secure a path for cars to be able to pass.
this constraint leads to no infeasible assignment.

## Slide 17: Weight balance of cargo
When the ship tilts, there is a possibility that the ship will lose its balance and roll over.
we add constraints for balance in two directions
  Forward and backward direction
  Left-right direction

## Slide 18: Rules for splitting orders
For large orders, we split them up.
  if the number of cars is over 500, we split the order in two.
  if the number of cars is over 1000, we split the order in three.
  If not, we do not split them up.

## Slide 19: Height of the hold
Each hold has height.
To place cars in holds, the height of the car needs to be lower than the height of the hold

## Slide 20: Computational experiment
With this model, we confirmed that we can get a good assignment for small bookings.
The number of orders and the number of loading and unloading ports increases, the calculations may not be sufficiently advanced in a limited time.[1]
[1]鵜川知哉, 自動車運搬船における貨物積載プラン ニングの席割問題に対する数理モデリング, 修士 論文，名古屋大学情報学研究科, 2020

## Slide 21: Computational experiment
We investigated how much the computation time changes by adding constraints.
We compared the case with and without considering the height constraint.
The booking we used has 109 orders, has 2 loading ports and 3 destination ports.

## Slide 22: comparison
Without height constraint
with height constraint
Calculation time | Objective's value | Lower bound
537 | 1035446 | -4461.98
933 | -4285 | -4461.98
2510 | -4301 | -4461.98
2973 | -4311 | -4461.98
Calculation time | Objective's value | Lower bound
3100 | 385282 | -4461.98
3128 | -4152 | -4461.98
8433 | -4173 | -4461.98
10484 | -4347 | -4461.98

## Slide 23: Computational experiment
We also try to investigate what scale of bookings can be solved in a limited time.
We set the limit time to 24 hours.

## Slide 24
Num of orders | Num of loading ports | Num of Destination ports | when a feasible solution was found. | Value after 1h | Lower bound after 1h | Value after 24h | Lower bound after 24h
109 | 2 | 3 | 537 | -4301.36 | -4461.98 | -4388.44 | -4461.98
109 | 2 | 5 | 1674 | -3522.82 | -4461.98 | -4264.69 | -4461.98
109 | 4 | 3 | 344 | -3515.46 | -4461.98 | -4365.89 | -4461.98
250 | 2 | 3 | 2381 | -3155.02 | -4461.98 | -4083.18 | -4461.98
350 | 2 | 3 | 2249 | -2738.00 | -4461.98 | -2883.58 | -4461.98

## Slide 25: Summary &future work
Summary
  It takes about three times as long when height constraints are taken into account.
  We can get good solutions for bookings which has less than 250 orders and has less than 2~5 ports.
Future work
  creating an index to evaluate the quality of the assignment
  Modifying the mathematical model
  Creating heuristic to be able to solve large bookings